## Slide 1: Data Communication and Networking (DCAN 202) Week 5

## Slide 2: Chapter 7, 8: Local Area Networks
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.

## Slide 3: Todays Lecture
Definition of a Local Area Network (LAN)
  List the primary function, activities, and application areas of a LAN
  Cite the advantages and disadvantages of LANs
Identify the physical and logical layouts (topologies) of LANs
Various medium access control techniques
Various IEEE 802 frame formats
Common local area network systems
  Compare and contrast wireless LANs to wired LANs
Identify the main functions of network operating systems
Compare and contrast the Windows Server family, Unix, Linux, and Mac OS X Server network operating systems

## Slide 4: Introduction
A local area network is a communication network that interconnects a variety of data communicating devices within a small geographic area and broadcasts data at high data transfer rates
Since the local area network first appeared in the 1970s, its use has become widespread in commercial and academic environments

## Slide 5: Primary Function of Local Area Networks
To provide access to hardware and software resources that will allow users to perform one or more of the following activities:
  Access to the Internet
  File serving
    A large storage disk drive acts as a central storage repository
  Print serving
    Providing the authorization to access a particular printer, accept and queue print jobs, and providing a user access to the print queue to perform administrative duties
  Database and application serving
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 6: Primary Function of Local Area Networks
To provide access to hardware and software resources that will allow users to perform one or more of the following activities:
  Manufacturing support
    LANs can support manufacturing and industrial environments
  Academic support
    In classrooms, labs, and wireless
  E-mail serving
    Interconnection between multiple systems
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
A Local Area Network interconnecting another local area network, the internet, and a mainframe computer

## Slide 7: Advantages and Disadvantages of Local Area Networks
Advantages
  Ability to share hardware and software resources
  Individual workstation might survive network failure
  Component and system evolution are possible
  Support for heterogeneous forms of hardware and software
  Access to other LANs and WANs (Figure 7-1)
  Private ownership (maybe a disadvantage)
  Secure transfers at high speeds with low error rates
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
Disadvantages
  Equipment and support can be costly
  Level of maintenance continues to grow
  Private ownership (lease option attractive for some)
  Some types of hardware may not interoperate
  Just because a LAN can support two different kinds of packages does not mean their data can interchange easily
  LAN is only as strong as its weakest link, and there are many links

## Slide 8: The First Local Area Network: The Bus/Tree
The original topology
Workstation has a network interface card (NIC) that attaches to the bus (a coaxial cable) via a tap
Data can be transferred using either baseband digital signals or broadband analog signals
Baseband signals are bidirectional and more outward in both directions from the workstation transmitting
Broadband signals are usually unidirectional and transmit in only one direction
  Because of this, special wiring considerations are necessary
Buses can be split and joined, creating trees
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
Simple diagram of a local area network bus topology

## Slide 9: A More Modern LAN : The Star-Wired Bus
Logically operates as a bus, but physically looks like a star
Star design is based on hub
  All workstations attach to hub
Unshielded twisted pair usually used to connect workstation to hub
Originally, hub takes incoming signal and immediately broadcasts it out all connected links
Hubs can be interconnected to extend size of network
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
Simple example of a star-wired bus LAN

## Slide 10: Star-Wired Bus (continued)
Modular connectors and twisted pair make installation and maintenance of star-wired bus better than standard bus
Hubs can be interconnected with twisted pair, coaxial cable, or fiber-optic cable
Biggest disadvantage: when one station talks, everyone hears it
  This is called a shared network
    All devices are sharing the network medium
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
Interconnection of three hubs in a star wired bus LAN

## Slide 11: Medium Access Control Protocols
How does a workstation get its data onto the LAN medium?
A medium access control protocol is the software that allows workstations to “take turns” at transmitting data
Two basic categories:
  Contention-based protocols
  Round-robin protocols
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 12: Contention-Based Protocols
Essentially first-come, first-served
Most common example is carrier sense multiple access with collision detection (CSMA/CD)
If no one is transmitting, workstation can transmit
If someone else is transmitting, workstation “backs off” and waits
If two workstations transmit at same time, collision occurs
  When two workstations hear collision, they stop transmitting immediately
  Each workstation backs off a random amount of time and tries again
  Hopefully, both workstations do not try again at exact same time
CSMA/CD is an example of a non-deterministic protocol
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 13: Contention-Based Protocols (continued)
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
Two workstations at opposite ends of a bus experiencing a collision

## Slide 14: Switches
The hub is a simple device that transmits an incoming frame out all the other ports on the hub
The switch has intelligence and can filter out and forward frames based on their NIC address
A switch maintains internal port table(s) that keep track of which frames arrived on which ports
Switches have eliminated many hubs
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
A switch interconnecting two LANs

## Slide 15: Switches (continued)
A switch observes each frame that arrives at a port, extracts the source address from the frame, and places that address in the port’s routing table
A transparent switch is found with CSMA/CD LANs
Workstations that connect to a hub are on a shared segment
Workstations that connect to a switch are on a switched segment
The backplane of a switch is fast enough to support multiple data transfers at one time
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
A switch interconnecting two LANs has two internal port tables

## Slide 16: Switches (continued)
A switch that employs cut-through architecture is passing on frame before entire frame has arrived at switch
Multiple workstations connected to a switch use dedicated segments
  This is a very efficient way to isolate heavy users from the network
Switches can allow simultaneous access to multiple servers, or multiple simultaneous connections to a single server
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
A switch with two servers allowing simultaneous access to two servers

## Slide 17: Isolating Traffic Patterns and Providing Multiple Access
Whether shared or dedicated segments are involved, the primary goal of a switch is to isolate a particular pattern of traffic from other patterns of traffic or from the remainder of the network
Switches, because of their backplane, can also allow multiple paths of communications to simultaneously occur
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
Workstations connected to a shared segment local area network

## Slide 18: Full-Duplex Switches
Allow for simultaneous transmission and reception of data to and from a workstation
This full-duplex connection helps to eliminate collisions
To support a full-duplex connection to a switch, at least two pairs of wires are necessary
  One for the receive operation
  One for the transmit operation
  Most people install four pairs today, so wiring is not the problem
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 19: Virtual LANs
Virtual LAN (VLAN) – logical subgroup within a LAN that is created via switches and software rather than by manually moving wiring from one network device to another
Even though employees and their actual computer workstations may be scattered throughout the building, LAN switches and VLAN software can be used to create a “network within a network”
A relatively new standard, IEEE 802.1Q, was designed to allow multiple devices to intercommunicate and work together to create a virtual LAN
Instead of sending technician to a wiring closet to move a workstation cable from one switch to another, an 802.1Q-compliant switch can be remotely configured by a network administrator
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
A switch with two VLANs configured

## Slide 20: Link Aggregation
Allows you to combine two or more links into one higher-speed link
Why would we want to do this?
  What if you want more bandwidth between a device and a switch?
  What if you want to provide a back-up link between a device and a switch?
  What if you want to provide a higher-speed connection to a server?
An IEEE protocol (802.3ad-2000) which typically runs in most LAN devices can support link aggregation
Link aggregation attempts to balance the flow of messages over the multiple paths, unless the flow of frames belong to a particular conversation; then the frames are sent over one of the links.
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 21: Spanning Tree Algorithm
What if you have a large set of networks interconnected with many switches?
Because of this large set of networks, a loop has been created in which a frame can circle through the networks and actually return to the originating device
The spanning tree algorithm (used in Spanning Tree Protocol and now Rapid Spanning Tree Protocol) runs in switches and can identify loops and remove them
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 22: Spanning Tree Algorithm
How does the spanning tree algorithm work? Four steps:
  Identify a switch as the root switch
  Visit each switch and identify the one port that has the shortest path back to the root switch. Mark these ports with RP (root port)
  Visit each LAN and identify the port that provides the shortest path back to the root switch. Mark these ports with a DP (designated port).
  Are there any ports remaining that don’t have either an RP or DP designation? Mark those ports as Removed. (They aren’t physically removed, only removed in the forwarding tables)
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
Network interconnection indicating root switch, root ports, designated ports, and removed connections

## Slide 23: Quality of Service
On a standard Ethernet LAN, all frames have the same priority, which is none
What if you want to make video-conferencing frames a higher priority than email frames?
You can use IEEE 802.1p standard which is installed in most if not all switches
The 802.1p standard adds a 3-bit field to the front of each Ethernet frame
This 3-bit field can be used to establish a priority
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 24: Wired Ethernet
Most common form of LAN today
  Star-wired bus is most common topology but bus topology still not totally dead yet
  Comes in many forms depending upon medium used and transmission speed and technology
Originally, CSMA/CD was 10 Mbps
  Then 100 Mbps was introduced
    Most NICs sold today are 10/100 Mbps
  Then 1000 Mbps (1 Gbps) was introduced
  10 Gbps is now being installed in high-end applications
  40 Gbps (GbE) and 100 GbE are now appearing in high-end switches and networks
1000 Mbps introduced a few interesting wrinkles:
  Transmission is full-duplex (separate transmit and receive), thus no collisions
  Prioritization is possible using 802.1p protocol
    Topology can be star or mesh (for trunks)
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 25: Wired Ethernet (continued)
One of the more recent features is power over Ethernet (PoE)
What if you have a remote device that has an Ethernet connection?
  It will require a power connection
What if you don’t have an electrical outlet nearby?
  Use PoE
    Power to drive Ethernet NIC is sent over wiring along with usual Ethernet signals
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 26: LANs In Action: A Small Office Solution
What type of system will interconnect 20 workstations in one room and 15 workstations in another room to a central server, which offers:
  Internal e-mail
  A database that contains all customer information
  High-quality printer access
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 27: LANs In Action: A Small Office Solution (continued)
Wiring diagram of an office space showing the placement of switches and servers
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 28: LANs In Action: A Small Office Solution (continued)
The modified network with a router and high-speed phone line
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 29: Wireless Ethernet
Not really a specific topology
  Workstation in a wireless LAN can be anywhere as long as it is within transmitting distance to an access point
Several versions of IEEE 802.11 standard define various forms of wireless LAN connections (we’ll take a look at these versions in a little bit)
Two basic components necessary:
  Client radio
    Usually a PC card with an integrated antenna installed in a laptop or workstation
  Access point (AP)
    An Ethernet port plus a transceiver
Access point acts as a bridge between the wired and wireless networks and can perform basic routing functions
Workstations with client radio cards reside within Basic Service Set, while multiple basic service sets create an Extended Service Set
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 30: Wireless Ethernet
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
A single-cell wireless LAN configuration
A multiple-cell wireless LAN configuration

## Slide 31: Wireless Ethernet
With directional antennae designed for point-to-point transmission (rare), 802.11b can transmit for more than 10 miles
With an omni-directional antenna on typical AP, range may drop to as little as 100 feet
IEEE 802.11n (100 Mbps theoretical) is the latest standard to be approved
802.11n uses MIMO technology (multiple input multiple output)
  Sender and receiver have multiple antennas for optimum reception
802.11ac uses advanced MIMO, wider channels in the 5 GHz band and advanced QAM techniques to achieve high data rates
  To provide security, most systems use either:
  Wired Equivalent Privacy (WEP) – provides either 40- or 128-bit key protection (dated)
  WPA or WPA 2 (Wi-Fi Protected Access)
  WPA 2 uses the most advanced encryption techniques
Wireless LANs may also be configured without an access point
  These configurations are called “ad-hoc”
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 32: Wireless CSMA/CA [carrier sense multiple access with collision avoidance]
CA (Collision avoidance)
  Protocol does not listen and detect collisions like CSMA/CD
  Instead, tries to avoid collisions before they happen
How does CSMA/CA do this?
  All devices, before they transmit, must wait an amount of time called an interframe space (IFS)
  Some applications have a short IFS, while others have a long IFS
    If two applications want to transmit at same time, the application with shorter IFS will go first
Note that the frame format for wireless Ethernet(CSMA/CA) has four address fields:
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.
The various fields of the CSMA/CA frame

## Slide 33
Flowchart showing the algorithm for CSMA/CA
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 34: LAN Support
Proper support of a local area network requires hardware, software, and miscellaneous support devices
Network OS is the most important software component
  Several popular network OSs currently exist:
    Windows Server family
    Unix
    Linux
    NetWare derivatives
Numerous network support programs are also required to support users on a LAN
  Support devices such as hubs, switches, routers, servers, modems, power supplies, and more are also necessary
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 35: Network Operating Systems
An OS manages all applications and resources in a computer
Multitasking OS supports execution of multiple processes at one time
Network OS is large, complex program that manages the resources common on most local area networks; client OS such as Windows 7 can perform some networking functions
Besides performing standard OS functions, a network OS is called upon for additional functions, such as:
  Manage one or more network servers
  Manage one or more network printers
  Manage the interconnection between LANs
  Manage locally connected users
  Manage remotely connected users
  Support system security
  Support client/server functions
  Support Web page development and Web server operations
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 36: Windows Server 2019
The latest version of Windows network OS
New server core (including a virtual server)
Self-healing server that can fix corrupted files and/or folders
Increased processing speed
Advancements in network security
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 37: Unix
Well established and very popular multitasking OS capable of supporting network operations
First OS written in the language C
Very stable system capable of supporting very large operations
Numerous versions available from different vendors
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 38: Linux
OS based on the principles of Unix.
Many versions available for free (Free Software Foundation’s GNU toolset) or very small price
Very stable multitasking OS
When incorporated with other free software products, such as the Apache Web server and Atipa’s BlueBird network management software, this system becomes extremely cost effective and powerful
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 39: Mac OS X Server
Apple Computer finally joined the NOS market with its Mac OS Server
Version X is based on Linux code
Very stable and quite powerful
While installed primarily in Apple networks, Mac OS X Server is also capable of supporting non-Apple networks
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 40: Network Servers
In order to support a network OS, you need one or more network servers
  Network servers are high-power workstations often with multiple processors, RAID, SCSI, and lots of memory and disk space
  Various forms of servers include server appliances, and server blades
Server virtualization allows you to create multiple servers in software all running on a single physical server
To protect the server from catastrophic disk failure, disk drives on most network servers support one of the redundant array of independent disks (RAID) techniques
  RAID is a collection of techniques for interfacing multiple hard disk drives to a computer
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 41: Client/Server Networks vs. Peer-to-Peer Networks
A clear majority of LANs are client/server networks
A client/server network has one or more network servers supporting the operations of one or more clients, or user workstations
Peer-to-peer networks also exist
  May have servers, but the network relies less on the servers and more on the communications between workstations
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 42: Server Software
Software necessary to support server side of Internet connections
Retrieves Web pages and other documents when asked to by a client workstation
Can interface with database program allowing users to store and retrieve data via Internet
Necessary with commercial Internet applications
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 43: Software Licensing Agreements
Virtually every commercial software program comes with a specific licensing agreement
Most licensing agreements specify the following conditions:
  Software installation and use
  Network installation
  Backup copies
  Decompilation
  Rental statement
  Upgrade availabilities
  Copyright restrictions
  Maintenance agreements
Most licensing agreements come in one of the following forms:
  Single-user-single-station license
  Single-user-multiple-station license
  Interactive user license
  Network server license
  Site license
  Corporate license
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 44: LANs In Action: A Home Office Solution
Sam has three computers at home and wants all three to share a printer and a connection to the Internet
What are some of the questions that Sam has to answer before he can start purchasing and/or installing something?
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.

## Slide 45: LANs In Action: A Home Office Solution
Many decisions to make when installing a wireless LAN
  Which IEEE 802.11 format?
    802.11a?
      Fast (54 Mbps), uses higher frequencies
    802.11g?
      Fast (54 Mbps), compatible with 802.11b
    802.11n or ac?
      Latest standards (100+Mbps)
  What type of wireless access point do you need?
    If you already have a wired network (with router and modem), all you need is a basic wireless access point
    If you don’t have a home network but have a high-speed Internet connection, you will need a wireless router
    If you don’t even have a high-speed Internet connection yet, you might want to consider a wireless gateway.
  What type of network OS do you need?
    Do you need something as powerful as Windows 2012 Server?
    No, you only need a client OS such as latest Windows desktop OS, Apple Mac OS, or Linux
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All Rights Reserved.