## Slide 1
Data Communication and Networking (DCAN 202)
Week 3
Kent Institute Australia Pty. Ltd.
ABN 49 003 577 302 CRICOS Code: 00161E RTO Code: 90458 TEQSA Provider Number: PRV12051
Version 2 – 18th December 2015

## Slide 2: Chapter 3: Conducted and Wireless Media
Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.

## Slide 3: Todays Lecture
Twisted-pair wire
  Characteristics, advantages, disadvantages
  Differences between Category 1, 2, 3, 4, 5, 5e, 6, and 7
  Shielded vs Unshielded twisted pair wire
Coaxial cable & Fiber-Optic cable
Microwave systems
  Terrestrial & Microwave
Basics of cellular telephones
Short-range transmission technologies (Bluetooth)

## Slide 4: Todays Lecture
Characteristics, advantages, and disadvantages of:
  Wireless Application Protocol (WAP),
  Broadband wireless systems, and
  Various wireless local area network transmission techniques
Media selection criteria of cost, speed, right-of-way, expandability and distance, environment, and security to various media in a particular application

## Slide 5: Introduction
The world of computer networks would not exist if there were no medium by which to transfer data
The two major categories of media include:
  Conducted media
  Wireless media

## Slide 6: Twisted Pair Wire
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.
Example of a four-pair twisted pair wire
One or more pairs of single conductor wires that have been twisted around each other
Twisted pair wire is classified by category.
  Currently Category 1 through Category 7
    Categories 1, 2 and 4 are nearly obsolete
Twisting the wires helps to eliminate electromagnetic interference between the two wires
Shielding can further help to eliminate interference

## Slide 7: Twisted Pair Wire
Parallel wires - greater chance of crosstalk
Perpendicular wires - lesser chance of crosstalk
Twisted wires - crosstalk reduced because wires keep crossing each other at nearly perpendicular angles
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.
Example of shielded twisted pair

## Slide 8: Twisted Pair Wire
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.
Summary of characteristics of twisted pair wires

## Slide 9: Twister Pair - Summary
Most common form of wire
Relatively inexpensive
Easy to install
Carries high data rates (but not the highest)
Can suffer from electromagnetic noise
Can be easily wire-tapped
Comes in shielded and unshielded forms

## Slide 10: Coaxial Cable
A single wire wrapped in a foam insulation surrounded by a braided metal shield, then covered in a plastic jacket.
  Cable comes in various thicknesses
Baseband coaxial technology uses digital signalling in which the cable carries only one channel of digital data
Broadband coaxial technology transmits analog signals and is capable of supporting multiple channels
Example of coaxial cable showing metal braid
Example of thick and thin coaxial cables
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.

## Slide 11: Coaxial Cable - Summary
A single wire surrounded by a braided shield
Because of shielding, can carry a wide bandwidth of frequencies
  Thus is good with applications such as cable television
Not as easy to install as twisted pair
More expensive than twisted pair

## Slide 12: Fiber-Optic Cable
A thin glass cable approximately a little thicker than a human hair surrounded by a plastic coating and packaged into an insulated cable
A photo diode or laser generates pulses of light which travel down the fiber optic cable and are received by a photo receptor
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.
Plain fibre-optic cable Vs Fibre-optic cable in an insulated jacket

## Slide 13: Fiber-Optic Cable (cont..)
Fiber-optic cable is capable of supporting millions of bits per second for 1000s of meters
Thick cable (62.5/125 microns) causes more ray collisions, so you have to transmit slower. This is step index multimode fiber. Typically use LED for light source, shorter distance transmissions
Thin cable (8.3/125 microns) – very little reflection, fast transmission, typically uses a laser, longer transmission distances; known as single mode fiber
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.
A fiber-optic cable with multiple strands of fiber

## Slide 14: Fiber-Optic Cable (cont..)
Fiber-optic cable is susceptible to reflection (where the light source bounces around inside the cable) and refraction (where the light source passes out of the core and into the surrounding cladding)
Thus, fiber-optic cable is not perfect either. Noise is still a potential problem
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.
A simple demonstration of reflection and refraction in a fiber-optic cable

## Slide 15: Fiber-Optic Cable (cont..)
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.
A fiber-optic backbone with Category 6 twisted pair running to the workstations

## Slide 16: Fiber-Optic Cable - Summary
Fiber optic cable can carry the highest data rate for the longest distances
Initial cost-wise, more expensive than twisted pair, but less than coaxial cable
But when you consider the superiority of fiber, initial costs outweighed by capacities
Need to fibers for a round-trip connection
Not affected by electromagnetic noise and cannot be easily wiretapped, but still noise

## Slide 17: Conducted Media
A summary of the characteristics of conducted media
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.

## Slide 18: Wireless Media
Radio, satellite transmissions, and infrared light are all different forms of electromagnetic waves that are used to transmit data
Technically speaking – in wireless transmissions, space is the medium
Note in the following figure how each source occupies a different set of frequencies
Electromagnetic Wave Frequencies
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.

## Slide 19: Terrestrial Microwave Transmission
Land-based, line-of-sight transmission
Approximately 20-30 miles between towers
Transmits data at hundreds of millions of bits per second
Signals will not pass through solid objects
Popular with telephone companies and business to business transmissions
A typical microwave tower and antenna
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.

## Slide 20: Terrestrial Microwave Transmission (continued)
A microwave antenna on top of a free-standing tower transmitting to another antenna on the top of a building.
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.

## Slide 21: Satellite Microwave Transmission
Similar to terrestrial microwave except the signal travels from a ground station on earth to a satellite and back to another ground station
Can also transmit signals from one satellite to another
Satellites can be classified by how far out into orbit each one is (LEO, MEO, GEO, and HEO)
Earth and the four Earth orbits: LEO, MEO, GEO, and HEO
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.

## Slide 22: Satellite Microwave Transmission (continued)
LEO (Low-Earth-Orbit) – 100 to 1000 miles out
  Used for wireless e-mail, special mobile telephones, pagers, spying, videoconferencing
MEO (Middle-Earth-Orbit) – 1000 to 22,300 miles
  Used for GPS (global positioning systems) and government
GEO (Geosynchronous-Earth-Orbit) – 22,300 miles
  Always over the same position on earth (and always over the equator)
  Used for weather, television, government operations
HEO (Highly Elliptical Earth orbit) – satellite follows an elliptical orbit
  Used by the military for spying and by scientific organizations for photographing celestial bodies

## Slide 23: Satellite Microwave Transmission (continued)
Satellite microwave can also be classified by its configuration
  Bulk carrier configuration
  Multiplexed configuration
  Single-user earth station configuration (e.g., VSAT)
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.
Bulk carrier facilities, multiplexed Earth station, and single-user Earth station configurations of satellite systems

## Slide 24: Cellular Telephones
Wireless telephone service, also called mobile telephone, cell phone, and PCS
To support multiple users in a metropolitan area (market), the market is broken into cells
Each cell has its own transmission tower and set of assignable channels
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.
One cellular telephone market divided into cells

## Slide 25: Cellular Telephones (continued)
Placing a call on a cell phone
  You enter a phone number on your cell phone and press Send. Your cell phone contacts the nearest cell tower and grabs a set-up channel. Your mobile identification information is exchanged to make sure you are a current subscriber.
  If you are current, you are dynamically assigned two channels: one for talking, and one for listening. The telephone call is placed. You talk.
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.
A cellular telephone tower

## Slide 26: Cellular Telephones (continued)
Receiving a call on a cell phone
  Whenever a cell phone is on, it “pings” the nearest cell tower every several seconds, exchanging mobile ID information. This way, the cell phone system knows where each cell phone is.
  When someone calls your cell phone number, since the cell phone system knows what cell you are in, the tower “calls” your cell phone.
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.
A cellular telephone tower

## Slide 27: WiMax - Broadband Wireless Systems
Delivers Internet services into homes, businesses and mobile devices
Designed to bypass the local loop telephone line
Transmits voice, data, and video over high frequency radio signals
Maximum range of 20-30 miles and transmission speeds in Mbps
IEEE 802.16 set of standards
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.
Broadband wireless configuration in a metropolitan area

## Slide 28: Bluetooth
Bluetooth is a specification for short-range, point-to-point or point-to-multipoint voice and data transfer
Bluetooth can transmit through solid, non-metal objects
Its typical link range is from 10 cm to 10 m, but can be extended to 100 m by increasing the power
Bluetooth will enable users to connect to a wide range of computing and telecommunication devices without the need of connecting cables
Typical uses include phones, pagers, modems, LAN access devices, headsets, notebooks, desktop computers, and PDAs

## Slide 29: Wireless Local Area Networks (IEEE 802.11)
This technology transmits data between workstations and local area networks using high-speed radio frequencies
Current technologies allow up to 100 Mbps (theoretical) data transfer at distances up to hundreds of feet
Three popular standards: IEEE 802.11b, a, g, n
More on this in Chapter Seven (LANs) (Week 5 Lecture)

## Slide 30: Free Space Optics
Free space optics
  Uses lasers, or more economically, infrared transmitting devices
  Line of sight between buildings
  Typically short distances, such as across the street
  Newer auto-tracking systems keep lasers aligned when buildings shake from wind and traffic

## Slide 31: Ultra-Wideband
Ultra-wideband
  UWB not limited to a fixed bandwidth but broadcasts over a wide range of frequencies simultaneously
  Many of these frequencies are used by other sources, but UWB uses such low power that it “should not” interfere with these other sources
  Can achieve speeds up to 100 Mbps but for small distances such as wireless LANs

## Slide 32: Infrared Transmissions
Transmissions that use a focused ray of light in the infrared frequency range
Very common with remote control devices, but can also be used for device-to-device transfers, such as PDA to computer

## Slide 33: Near-Field Communications
Very close distances or devices touching
Magnetic induction (such as radio frequency ID) used for transmission of data
Commonly used for data transmission between cellphones (non-Apple devices)

## Slide 34: ZigBee
Based upon IEEE 802.15.4 standard
Used for low data transfer rates (20-250 Kbps)
Also uses low power consumption
Ideal for heating, cooling, security, lighting, and smoke and CO detector systems
ZigBee can use a mesh design – a ZigBee-enabled device can both accept and then pass on ZigBee signals

## Slide 35: Media Selection Criteria
Cost
  Different types of costs
    Initial cost – what does a particular type of medium cost to purchase? To install?
    Maintenance / support cost
  ROI (return on investment) – if one medium is cheaper to purchase and install but is not cost effective, where are the savings?
Speed
Distance and expandability
Environment
Security

## Slide 36: Media Selection Criteria
Cost
Speed
  Two different forms of speed:
    Propagation speed – the time to send the first bit across the medium
      This speed depends upon the medium
      Airwaves and fiber are speed of light
      Copper wire is two thirds the speed of light
    Data transfer speed – the time to transmit the rest of the bits in the message
      This speed is measured in bits per second
Distance and expandability
Environment
Security

## Slide 37: Media Selection Criteria
Cost
Speed
Distance and expandability
  Certain media lend themselves more easily to expansion
  Don’t forget right-of-way issue for conducted media and line-of-sight for certain wireless media
Environment
Security

## Slide 38: Media Selection Criteria
Cost
Speed
Distance and expandability
Environment
  Many types of environments are hazardous to certain media
    Electromagnetic noise
    Scintillation and movement
    Extreme environmental conditions
Security

## Slide 39: Media Selection Criteria
Cost
Speed
Distance and expandability
Environment
Security
  If data must be secure during transmission, it is important that the medium not be easy to tap
    Make the wire impervious to electromagnetic wiretapping
    Encrypt the signal going over the medium

## Slide 40: Wireless Media In Action: Three Examples
First example – you wish to connect two computers in your home to Internet, and want both computers to share a printer
  Can purchase wireless network interface cards
  May consider using Bluetooth devices
Second example – company wants to transmit data between two locations, Chicago and Los Angeles
  Company considering two-way data communications service offered through VSAT satellite system
VSAT satellite solution for DataMining Corporation
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.

## Slide 41: Wireless Media In Action: Three Examples (continued)
Third example – second company wishes to transmit data between offices two miles apart
  Considering terrestrial microwave system
Microwave communication between American Insurance’s corporate buildings
Source: Data Communications and Computer Networks: A Business User's Approach, Eighth Edition
© 2016. Cengage Learning. All right reserved.

## Slide 42: Summary
All data communication media can be divided into two basic categories: (1) physical or conducted media, and (2) radiated or wireless media, such as satellite systems
The three types of conducted media are twisted pair, coaxial cable, and fiber-optic cable
Twisted pair and coaxial cable are both metal wires and are subject to electromagnetic interference
Fiber-optic cable is a glass wire and is impervious to electromagnetic interference
  Experiences a lower noise level
  Has best transmission speeds and long-distance performance of all conducted media

## Slide 43: Summary (continued)
Several basic groups of wireless media exist: terrestrial microwave transmissions, satellite transmissions, cellular telephone systems, infrared transmissions, WiMAX, Bluetooth, Wi-Fi, free space optics, ultra-wideband, near-field communications, and ZigBee
Each of the wireless technologies is designed for specific applications
When trying to select particular medium for an application, it helps to compare the different media using these six criteria: cost, speed, expandability and distance, right-of-way, environment, and security

## Slide 44: kent.edu.au Kent Institute Australia Pty. Ltd. ABN 49 003 577 302 ● CRICOS Code: 00161E ● RTO Code: 90458 ● TEQSA Provider Number: PRV12051